DIVISION 8

SECTION 08300

SPECIALTY DOOR SYSTEMS

PART 1- GENERAL

1.01 SECTION INCLUDES

A.	ENVIRO Infitting Hinged Metal doors and accessories for complete installation.

1.02 RELATED SECTIONS

A.	Division 16 - Electrical.

1.03 SUBMITTALS

A.	Product Data: Completely describing components.

B.	Shop Drawings: Showing details of fabrication, installation and accommodation to connecting work.

C.	Installation Instructions: For door, operator and accessories.

D.	Operating and Maintenance Data: For door, operator and accessories.

1.04 QUALITY ASSURANCE

A.	Installer Qualification: Door manufacturer, or trained, approved and licensed door installer.

PART 2 - PRODUCT

2.01 MANUFACTURERS

A.	ENVIRO Model 413 Infitting Hinged Metal doors as manufactured by ASI Doors, Inc., Milwaukee, Wisconsin.

- Substitutions:

No substitution will be considered unless written request for approval has been submitted by the bidder and has been received by the architect at least ten (10) days prior to the date for receipt of bids.

Each such request shall include the name of the materials for which it is to be substituted and a complete description of the proposed substitute including drawings, cuts, mock-ups, performance and test data, a list of projects of similar scope and photographs of existing installations, and any other information necessary for evaluation.

2.02 INFITTING HINGED METAL DOORS

A.	ENVIRO Model 413 Infitting Hinged Door.

- Door size to fit door opening as shown on architectural drawings and to conform to APHIS-U.S.D.A. (M.I.D.) sanitation regulations.

- Doors shall be manually operated, infitting hinged (cooler or freezer) doors.

- Door panel shall consist of a white stucco-embossed steel skin, filled with polyurethane insulation, to a finished thickness of 4” or 6”. (Optional galvanized or stainless steel skin available.)

- Internal frame to have an interlocking perimeter and complete wood-free structure.

- Flat face door frame consists of 24 gauge, smooth white steel formed to a thickness of 1-5/8”, with high density polyethylene backing at all anchor locations. (Optional galvanized or stainless steel frames available.)

- Standard door hardware includes a chrome latch, strike and 9” polished aluminum cam-lift hinges. (Optional powder coated or stainless hardware available)

- Door latch has padlock provision to permit door to be opened from inside, even when locked from outside.

- Gaskets to be full perimeter high compression EPDM rubber.

- Freezer doors to be equipped on three sides of frame and the bottom of door with heater wire.

Note: Specify 6" of insulation for all blast freezer applications; or when temperature difference between rooms is more than 50(F.

PART 3 - EXECUTION

3.01 EXAMINATION

A.	Verify installation conditions as satisfactory to receive work of this section.  Do not install until unsatisfactory conditions are corrected. Beginning work constitutes your acceptance of conditions as satisfactory.

1.	Verify opening size, dimensions and tolerances.

3.02 PREPARATION

- Protect surrounding areas and surfaces to prevent damage during work of this section.

3.03 INSTALLATION

- Install the work in accordance with manufacturer instructions.

- All electrical high power and low voltage wiring to be supplied, installed and connections to doors are to be by electrical contractor.

- Wall construction (by others) to be sufficient to support the door assembly and to support the operation of the door panel.

3.04 WARRANTIES

A.	One year limited warranty on all components.

3.05 CLEANING

- Leave the premises clean and free of residue of work of this section.

END OF SECTION